## Slide 1: Effective prevention from Legionella bacteria

## Slide 2: What is it?
Confidential
Legionnaire's disease is an infectious disease that affects the respiratory system.
Legionellas prefer natural and artificial reservoirs, and temperatures between 25 and 55 °С.

## Slide 3
Confidential
High
temperature
Required
temperature
Low
temperature
Insufficient
temperature

## Slide 4: WHICH ARE THE MAIN PROBLEMS?
Confidential
-From low temperatures
-From high temperatures

## Slide 5: From low temperatures
Confidential
Risk of Legionella
Energy costs
Waiting time of hot water
Waste of water

## Slide 6: From high temperatures
Confidential
Waste of energy
Corrosion and limescale
Burning of hot water

## Slide 8
Confidential

## Slide 9: SOLUTION?
Confidential
-
Chemical methods(chlorination, ozoning. Both influence negative on the water quality and corrosion)
Physical methods(thermal disinfection, ultravioletlight)
High temperatures is by far the easiest and most reliable way to disinfect the system(65ºC kills all bacteria in ~10 minutes)

## Slide 10: Cim 778 Thermostatic regulator
For domestic hot water recirculation loops
Confidential
With disinfection function against LEGIONELLA

## Slide 11: Features
The thermostatic regulator, installed on each branch of the recirculation circuit, automatically maintains the set temperature. This device modulates the medium flow rate in accordance with the water inlet temperature by means of the action of a dedicated internal thermostatic cartridge.
It is also equipped with a by-pass mechanism, to be used in the event of thermal disinfection against Legionella.
Confidential

## Slide 12: Operating principle
When the water temperature approaches the set value, the obturator progressively reduces the passage. The medium flow rate supplied by the recirculation pump is thus distributed to the other network branches, resulting in effective automatic thermal balancing.
If necessary, the regulator is already designed with a thermal disinfection function, which is useful if the system temperature is to be increased to values over 55–60°C (130-140 °F). This function is completely automatic, activated by the inner sensor that opens a by-pass at ≂70°C (≂160°F).
Confidential

## Slide 13: Setting
Setting of required Temperature with scale dial.
Confidential

## Slide 14: Temperature control
Cold Water = max flow
Water at setting temperature = minimum flow
Confidential
*binder points are optional

## Slide 15: Disinfection against Legionella
Water at ≂70°C (≂160°F).
= disinfection against legionella =By-Pass
Confidential
*binder points are optional

## Slide 16: Flow rates
Confidential
Example
Setting 51 °C

## Slide 17: Typical installation – without Cim 778

## Slide 18: Typical installation – with Cim 778

## Slide 19: Benefits
Easy temperature adjustment;
Energy saving thanks the auto-balancing feature
Built-in disinfection function to protect against legionella
Available in 3 sizes (1/2”,3/4”,1”) for different flow rates
DZR Brass body
Confidential

## Slide 20: Accessories
Cim 999CS - Thermometer
Cim 728C –Insulating case
Cim 723L – Binder points